## Slide 1: String Material Properties’ Effect on Sound
Laboration and Computer Analysis using Python
Group 9 - Yilai Chen & Bartosz Brzuchalski

## Slide 2: Laboration Setup
• Location: Speech, Music, and Hearing Department at KTH
• Equipment: Suspension mechanism, condenser microphone, audio interface, computer (Audacity)
• Procedure:
- Strings mounted individually and tuned to D2 or D3
- Microphone placed ~1.5 cm above string
- Plucking performed at 1/8th of string length (65 cm)
- Recorded at 44100 Hz sample rate, processed in Logic Pro
- Dynamics: mp, mf, f

## Slide 3: Strings Used
Unison Strings:
• Gut
• Nylgut
• Nylon
• Steel
Wound Strings:
• Silk
• Nylgut
• Nylon
• Roundwound
• Flatwound

## Slide 4: Computer Analysis using Python
Tasks:
• Waveform Plotting
• Spectral Analysis (Partial Tones Detection)
• Amplitude Envelope Estimation
• Inharmonicity Coefficient Calculation
Libraries: librosa, scipy, matplotlib

## Slide 5: Waveform Plotting
• Used librosa.load to read audio data.
• Generated time vector and plotted waveform using matplotlib.
• Visualizes amplitude variations over time.

## Slide 6: Spectral Analysis (Partial Tones Detection)
• Applied Short-Time Fourier Transform (STFT).
• Used scipy.signal.stft for frequency analysis.
• Detected peaks with scipy.signal.find_peaks.
• Spectrograms displayed with librosa.display.specshow.

## Slide 7: Amplitude Envelope Estimation
• Estimated amplitude envelopes of partial tones.
• Fitted exponential decay models to amplitude data:
envₙ(t) = Aₙ * exp(-γₙ * t)
• Plotted decay rates to observe damping characteristics.

## Slide 8: Inharmonicity Coefficient Calculation
• Measured deviation of overtones from harmonic frequencies.
• Formula:
fₙ = n f₀ √(1 + n² Bₙ), where
Bₙ = ((fₙ / (n f₀))² - 1) / n²
• Plotted inharmonicity variation across harmonics.